## Slide 1: Lightweight assistive technology: A wearable, optical-fiber gesture recognition system
Sanjay Seshan

## Slide 2: Motivation

## Slide 3: Basic idea
Transverse carpal ligament area
  Deflection occurs when fingers [tendons] are moved
How to measure deflection?
  Light

## Slide 4: Basic setup for an optic fiber
Fiber/light medium
LED
Photoresistor/LDR
LED
Photoresistor/LDR
In order to detect the deflection using a LDR, a significant amount of light must be lost when the fiber is bent

## Slide 5: Materials/Mediums proposed
Standard optical fiber
Vytaflex – a semi-transparent urethane rubber
Ecoflex – an opaque silicone
Humimic gel – a transparent synthetic gelatin

## Slide 6: Testing process
Consistent 3d printed to isolate light
Holder for LED and LDR on each end
Plastic piece for consistent depression of medium

## Slide 7: LED Color
The optimal wavelength of the LDR must be determined
This does not depend on the material used
Humimic was used as a constant baseline
A 3d printed cast was used to eliminate external light
A constant depression was used to determine minimum intensity
Colour | Medium | Minimum Intensity | Maximum Intensity | delta Intensity | Notes
Large blue | Humimic #2 | 160 | 993 | 833 | 
Large red | Humimic #2 | 183 | 1013 | 830 | 
Large white | Humimic #2 | 205 | 1021 | 816 | 
Small red | Humimic #2 | 180 | 977 | 797 | 
Large red | Earth's atmosphere | 235 | 996 | 761 | Value seems to fall slowly
Large yellow | Humimic #2 | 210 | 971 | 761 | 
Small green | Humimic #2 | 189 | 937 | 748 | 
Large blue | Earth's atmosphere | 228 | 957 | 729 | 
Large green | Humimic #2 | 185 | 850 | 665 | Value seems to fall rapidly
Small red | Earth's atmosphere | 245 | 864 | 619 | Value seems to fall slowly
Small green | Earth's atmosphere | 253 | 775 | 522 | 
Large green | Earth's atmosphere | 240 | 720 | 480 | Value seems to fall rapidly

## Slide 8: Problems with each material
Optic fibers were too perfect and there was no light deflection, even when bent over 90 degrees.
  The internal reflection is too high
  A non-ideal optical fiber is needed so that light is lost when bent
Ecoflex was too opaque and did not permit any light from the LED to pass
Humimic was too soft and melted/tore due to the body heat.
  Humimic melts at about 50 degrees; body heat is about 40

## Slide 9: Gestures tested
Finger Extension [Extend]
Finger Flexion [Fist]
One
Two

## Slide 10: Collecting data
1 Arduino Uno
5 LDRs and 5 10k Ohm resistors
LED circuit:
  9V battery, 5V regulator, 2 XXX resistors, 5 LEDs

## Slide 11: Different shapes tested
Tube
  Shrink tube: 20mm, 5mm, 4mm
  3d print: 2mm, 4mm, 5mm
  Straws: 3mm, 5mm
Sinusoidal  manufactured by first casting a mold using Vytaflex (Silicone)
Rectangular
Minimize the diameter to keep multiple strands for higher resolution
Sinusoidal and Rectangular molds required sensors to be embedded = fragility
Shrink tube and 3d printed molds caused capillary action (the material stuck to the sides)
Straws proved to be the best mold – 3mm proved to be best for LED shape and resolution

## Slide 12: Sample data: one
Chart: Light Intensity vs. Time (s)
Chart: ldr5 Intensity vs. Time (s)

## Slide 13: Cleaning up data
Use moving averages
3 are used to find the maximum, minimum, and transition period
This is used to label the data
Chart: Moving averages of ldr5 vs Time

## Slide 14: Labelling the data
Compare individual moving averages to original
Chart: Averaged light intensity vs. time
Time of determined maximum
Time of determined transition
Time of determined minimum