## Slide 1: Lightweight assistive technology: A wearable, optical-fiber gesture recognition system
Sanjay Seshan Fox Chapel Area High School

## Slide 2: Objectives
18 years ago, a movie called Minority Report was first to introduce the world to a gesture-based interactive device.
Though common in science fiction and comic book movies, it is yet to become reality.
The goal of this project it to build a lightweight, low powered method to interact with computers around us
The computer will recognize a wide range of hand gestures
Does not require the use or special gloves or other intrusive hardware
Notes: Minority report

## Slide 3: CURRENT methods VS. Requirements
Current methods are
  Intrusive and cumbersome to wear (unnatural positions) – Tap, Cyber Glove, and other devices are uncomfortable and hard to put on and take off
  Impractical – camera may not face the wearer, Google radar system is also off-body
  Prices range from $150 to $30,000
Must be wearable
Must be non-intrusive
Must be intuitive
Must be lightweight
Must be low-powered
Must be inexpensive
Tap
Cyber Glove
Notes: https://en.wikipedia.org/wiki/Wired_glove
https://www.youtube.com/watch?reload=9&v=mpbWQbkl8_g#t=810
https://towardsdatascience.com/training-a-neural-network-to-detect-gestures-with-opencv-in-python-e09b0a12bdf1
READ: https://www.wired.com/story/how-i-became-a-robot-in-london/

## Slide 4: Solution:
OPTIAssist: Optical Fiber Based Lightweight Assistive Technology
Strap around the wrist
  1 in 6 adults own a smart watch
Use optical fibers as sensors along the strap to detect deflection
Transverse carpal ligament area
  Deflection occurs when fingers [tendons] are moved
  Magnitude of deflection of different tendons can be used to identify gestures
  6 different tendons in wrist
How to measure deflection accurately?
  Must measure all tendons and measure tiny (< 1 mm) movement
  Deploy a set of sensors across a watch strap

## Slide 5: Optical Fibers as Sensors
Optical fibers rely on the concept of total internal reflection to cause light to travel from one end of the fiber to the other
The refractive index of the material is determined by the ratio of the speed of light in the medium to a vacuum:
The angle at which total internal reflection occurs is:
For most glass fiber optics and , therefore
Notes: https://www.flickr.com/photos/brixendk/4349817216
Note that , which is almost the same as a vacuum (), so
https://www.flickr.com/photos/brixendk/4349817216
Note that 𝜈_𝑎𝑡𝑚𝑜𝑠𝑝ℎ𝑒𝑟𝑒=1.000350, which is almost the same as a vacuum (𝜈_𝑣𝑎𝑐𝑢𝑢𝑚=1), so 𝜃≈𝑎𝑟𝑐𝑠𝑖𝑛(1/𝜈_𝑚𝑒𝑑𝑖𝑢𝑚 )

## Slide 6: Optical Fibers as Sensors (continued)
If light strikes the fiber-atmosphere boundary at less than the critical angle it is completely reflected
Imperfections and rough surfaces within the fiber can cause light to be scattered and lost
This loss is made worse when the fiber is bent or deflected
If fibers were embedded in a wrist strap, deflection due to hand movement would cause characteristic changes in the amount of light transmitted
Analyzing the transmitted light levels could allow computers to reconstruct gestures!
“Lost” Light
“Transmitted” Light

## Slide 7: Basic setup for Deflection Sensor
Fiber/light medium
LED
Photoresistor / Light Dependent Resistor (LDR)
LED
Photoresistor/LDR
In order to detect the deflection using an LDR, a significant amount of light must be lost when the fiber is bent
35mm fiber length was determined to be the minimum for a noticeable light deflection when bent

## Slide 8: PROJECT METHODOLOGY
Phase 1:
Proof of Concept
Phase 2:
Prototype
Determine best material
Determine best shape
Determine color of LED light
Create a wearable band
Add sensors
Develop data collection method
Phase 3:
Data Analysis
Measure how light levels are impacted by gestures
Uniquely identify different a selection of gestures
Automate process

## Slide 9: PHASE 1: Proof of CONCEPT
Designed a hard casing using SolidWorks to test concept
3D Printed design for consistency and durability
Key features
  A holder for the medium to be placed in
  Lid to eliminate external light and isolated LED light
  Holder for LED and LDR on each end
  Plastic tool for consistent depression of medium
HARDWARE
Tool
Lid
Holder
LDR
LED
Medium
Lid
Tool
Holder

## Slide 10: PHASE 1: Proof of concept
The optimal wavelength for the Light Dependent Resistor (LDR) depends on the type of LDR used
For my Cadmium Sulfide LDR, Large red (630nm) and large blue (460nm) LEDs were determined to be the best (had the greatest delta intensity when depressed).
Red was chosen due to availability.
Light Colors Tested
Colour | Medium/Fibre material | Minimum Intensity | Maximum Intensity | delta Intensity
Large blue | Humimic #2 | 160 | 990 | 830
Large red | Humimic #2 | 183 | 1013 | 830
Large white | Humimic #2 | 205 | 1021 | 816
Small red | Humimic #2 | 180 | 977 | 797
Large red | Earth's atmosphere | 235 | 996 | 761
Large yellow | Humimic #2 | 210 | 971 | 761
Small green | Humimic #2 | 189 | 937 | 748
Large blue | Earth's atmosphere | 228 | 957 | 729
Large green | Humimic #2 | 185 | 850 | 665
Small red | Earth's atmosphere | 245 | 864 | 619
Small green | Earth's atmosphere | 253 | 775 | 522
Large green | Earth's atmosphere | 240 | 720 | 480

## Slide 11: PHASE 1: proof of concept
Standard optical fiber
  Could not measure any light deflection
Ecoflex – an opaque silicone
  Too opaque and did not permit any light from the LED to pass
Humimic gel – a transparent synthetic gelatin
  Too soft. Melted even at body heat
Vytaflex – a semi-transparent urethane rubber
  Worked the best. Transmitted light the best and sturdy.
Mediums Tested
Materials: Ecoflex, Humimic, Vytaflex, optical fiber

## Slide 12: PHASE 1: proof of concept
Fiber Shapes
Tube Molding Material | Pros | Cons
Shrink tube (20mm, 5mm, 4mm) | Somewhat easy to obtain, many sizes | Material stuck to sides Did not mold well
3D Printed Tube (2mm, 4mm, 5mm) | Customizable | Material stuck to sides Material could not be removed
Straw Mold Tube (3mm, 5mm) | Easy to obtain 3mm proved to be best for LED shape and resolution | 5mm proved to be too thick and inflexible
Rectangular | Easier to fabricate | sensors have to be embedded = fragile
Sinusoidal | Degree of light path independence between sensors | Sensors have to be embedded = fragile
molds: Straws, heat shrink, 3d printed

## Slide 13: PHASE 2: prototype HARDWARE
Three 35mm and two 80mm Vytaflex fibers molded using 3mm straw
Large red (630nm) LEDs
LEDs and LDRs are fastened using heat shrink to the fiber
1 Arduino Uno
5 LDRs and 5 10k Ohm resistors
LED circuit: 9V battery, 5V regulator, 50 ohm resistor, 100 ohm resistor, Ohms resistors, 5 LEDs
35mm fibers
80mm fibers
LEDs
LDRs
1cm separation between fibers
1
5
2
3
4

## Slide 14: PHASE 2: ACTUAL HARDWARE SETUP
Setup on the previous slide is mounted with Velcro bands
The band is placed on the wrist
The Arduino is used to collect data
Code written in Python and C++
Arduino
Wrist strap

## Slide 15: PHASE 2: Gestures tested
A large collection of gestures can be tested using the prototype
I focus this presentation on three gestures
Finger Extension [Extend]
Finger Flexion
[Fist]
One Finger
[One]

## Slide 16: PHASE 3: DATA ANALYSIS
Light Intensity over Time
Manually Label Hand Position
Moving Averages vs. Original
Compute the Gestures
5 seconds of data was collected for each gesture
Includes a brief relax and transition period before and after gesture
Approximately 1 reading per 0.02s (250 readings/s)
Light intensity in scaled units (0 to 1023) based on the voltage drop due to the LDR (0 to 5V)
Compare

## Slide 17: PHASE 3: Data ANALYSIS [one finger]
Each sensor (LDR) has its own unique baseline intensity value
  Each sensor need to be calibrated to a specific value separately
Each sensor detects the change in intensity when hand gestures are made
Chart: Light Intensity for Repeated One Finger Gesture
Chart: Time (seconds)
Relax position
One finger position

## Slide 18: PHASE 3: Handling Changing Readings
The baseline readings for a sensor can change over time
  E.g., due to movement of the wristband
Need to distinguish between changes due to gestures and changes in the baseline
Two techniques to establish a baseline
Exponentially-weighted Moving Average: I use a moving average remove outliers and smooth noisy data
  determines how many “past values” to include in the average
    Small weighs past readings heavily
    Large makes the average closely track the current reading
    Tuning to 0.2 worked well
Sliding Window: I keep track of the maximum reading in the past 4 seconds. This followed the changing reading well
Chart: Time

## Slide 19: PHASE 3: Identifying a Single Gesture
Readings of two sensors “normalized” by subtracting the average value of their readings (i.e. centering graph around value of 0)
Some sensors react more significantly to specific gestures
  Sensor 5 detects the deflection more intensely than sensor 1
By examining the magnitude of the change across all sensors, a unique pattern can be determined for each type of gesture
Chart: Light Intensity for Repeated One Finger Gesture
Notes: Normalized Light Intensity

## Slide 20: PHASE 3: Creating a Gesture “Signature”
For each gesture, I manually labeled the data readings of a single trace as “Relax Baseline”, “Transition Between Relax and Gesture” and “Gesture” periods
I computed a simple average () reading of each period
I then computed the difference in Light Intensity between a Relax period and the subsequent Gesture period
This was done for each sensor and for each gesture
The table shows the average difference for each sensor/gesture
From this, I chose to use Sensors 2,3 and 4 to identify gestures
Chart: Time (seconds)
Relax
Gesture
Transition
Difference
 | Sensor 1 | Sensor 2 | Sensor 3 | Sensor 4 | Sensor 5
Extend | 8 | -48 | -90 | -223 | -12
Fist | 12 | -34 | -32 | -60 | 1
One | -3 | 2 | -24 | -49 | -4

## Slide 21: Conclusions and next steps
Fiber optics is a practical method of detecting deflection in the wrist
The project is a promising first step in creating a light-weight assistive technology
The next step of the project is to increase the number of gestures recognized and compete the machine learning training on the data to auto-detect gestures
The final design for the wrist strap will be to have the system in a watch band and powered by a smart watch rather than an Arduino

## Slide 22: code
int sensorPin = A0; // select the input pin for LDR(s)
int sensorPin2 = A1;
int sensorPin3 = A2;
int sensorPin4 = A3;
int sensorPin5 = A4;
int sensorValue = 0; // variable(s) to store the value coming from the sensor
int sensorValue2 = 0;
int sensorValue3 = 0;
int sensorValue4 = 0;
int sensorValue5 = 0;
void setup() {
Serial.begin(9600); //sets serial port for communication
pinMode(LED_BUILTIN, OUTPUT);
}
void loop() {
sensorValue = analogRead(sensorPin); // read the value(s) from the sensor(s)
sensorValue2 = analogRead(sensorPin2);
sensorValue3 = analogRead(sensorPin3);
sensorValue4 = analogRead(sensorPin4);
sensorValue5 = analogRead(sensorPin5);
Serial.print(sensorValue); //prints the values coming from the sensors on the screen
Serial.print(",");
Serial.print(sensorValue2);
Serial.print(",");
Serial.print(sensorValue3);
Serial.print(",");
Serial.print(sensorValue4);
Serial.print(",");
Serial.println(sensorValue5);
}
C++ Arduino Code

## Slide 23: code
#!/usr/bin/python
import serial
import time
import sys
# Determine the file to save data to and Arduino port
fileOut = sys.argv[2]
port = sys.argv[1]
f = open(fileOut, "w")
# Open Arduino serial
ser = serial.Serial(port, 9600, timeout=1)
def getData(timeout, label):
# measure delta time of a single gesture cycle for timeout
timeI = time.time()
while time.time()-timeI < timeout:
Python data collector:
Python data collector

## Slide 24: code
try:
reading = ser.readline() # Read sensor values from Arduino
# Record delta Time, Unix time, ldr readings, and label to a file
data = [0,0,0,0,0,0,0,""]
data[0] = time.time()-timeIA
data[1] = time.time()
data[2] = int(reading.split('\n')[0].split(",")[0])
data[3] = int(reading.split('\n')[0].split(",")[1])
data[4] = int(reading.split('\n')[0].split(",")[2])
data[5] = int(reading.split('\n')[0].split(",")[3])
data[6] = int(reading.split('\n')[0].split(",")[4])
data[7] = label
for i in data:
print str(i)+",",
f.write(str(i)+",")
print ""
f.write("\n")
except:
pass
Python data collector cont.

## Slide 25: code
gestures = ["extend","fist","one"]*2 # declare labels of which gestrues are being tested
print("delta Time, Unix Time, pr1, pr2, pr3, pr4, pr5, label") # file headers
f.write("delta Time, Unix Time, pr1, pr2, pr3, pr4, pr5, label\n")
# Collect data for each gesture cycle for 5.0s
timeIA = time.time()
for gesture in gestures:
continueQ = raw_input("Do "+gesture+"? [Y/n]: ")
if continueQ == "y" or continueQ == "" or continueQ == "Y":
getData(5.0, gesture)
elif continueQ == "n" or continueQ == "N":
continueQ = "n"
f.close()
Python data collector:
Python data collector cont.

## Slide 26: bIBLIOGRAPHY
To, Celeste, Tess Lee Hellebrekers, and Yong-Lae Park. "Highly Stretchable Optical Sensors for Pressure, Strain, and Curvature Measurement."
Meerbeek, I. M. Van, et al. “Soft Optoelectronic Sensory Foams with Proprioception.” Science Robotics, Science Robotics, 28 Nov. 2018, robotics.sciencemag.org/content/3/24/eaau2489.abstract.
Cho, Haedo, et al. "Design of an optical soft sensor for measuring fingertip force and contact recognition." International Journal of Control, Automation and Systems 15.1 (2017): 16-24.
Butt, Jawad Mehmood, Hesheng Wang, and Radan Pathan. "Design, Fabrication, and Analysis of a Sensorized Soft Robotic Gripper." 2018 IEEE 8th Annual International Conference on CYBER Technology in Automation, Control, and Intelligent Systems (CYBER). IEEE, 2018.
Chen, Wenbin, et al. "Fabrication and Dynamic Modeling of Bidirectional Bending Soft Actuator Integrated with Optical Waveguide Curvature Sensor." Soft robotics (2019).
Heintz, Brenner. “Training a Neural Network to Detect Gestures with OpenCV in Python.” Medium, Towards Data Science, 17 Dec. 2018, towardsdatascience.com/training-a-neural-network-to-detect-gestures-with-opencv-in-python-e09b0a12bdf1.
Poupyrev, Ivan. “Google I/O 2015.” Google, Google I/O Conference, 2015, www.youtube.com/watch?reload=9&v=mpbWQbkl8_g#t=810.

## Slide 27: Photo credit
https://orthoinfo.aaos.org/en/diseases--conditions/carpal-tunnel-syndrome/
https://www.semanticscholar.org/paper/Wrist-worn-hand-gesture-recognition-based-on-Zhu-Jiang/
https://thegadgetflow.com/
http://hyperphysics.phy-astr.gsu.edu/hbase/optmod/fibopt.html
http://oer2go.org/mods/en-boundless/www.boundless.com/physics/textbooks/boundless-physics-textbook/geometric-optics-24/reflection-refraction-and-dispersion-169/total-internal-reflection-and-fiber-optics-609-6258/index.html
https://en.wikipedia.org/wiki/Wired_glove
https://www.flickr.com/photos/brixendk/4349817216
https://www.amazon.com/
https://www.adafruit.com/
Minority Report (2002 Movie)
Sanjay Seshan

## Slide 28: Handling a mixture of gestures (continued)
The prototype was taken off then put back on later to determine consistency
The data was again labelled by hand and sorted by label
An example normalized average is shown below
Chart: Averaged light intensity vs. time (set 2)
Gesture | Delta ldr1 | Delta ldr2 | Delta ldr3 | Delta ldr4 | Delta ldr5
Extend | 5.111665 | -29.9195 | -84.9943 | -225.216 | -14.1436
Extend | 9.410196 | -42.6565 | -87.3831 | -197.826 | -11.6027
Fist | 10.98991 | -28.4957 | -29.111 | -42.4561 | 4.072323
Fist | 7.010972 | -32.6319 | -28.7861 | -31.4276 | 0.527709
One | -3.97222 | 6.715278 | -25.9514 | -57.3194 | -5.92361
One | 2.735097 | -1.79024 | -46.5674 | -58.7466 | -3.4117

## Slide 29: Handling a mixture of gestures
The order of the gestures tested was: extend  fist  one done twice
Labelled manually as the gesture, relax, or transition
The data was normalized by finding the delta intensity from the last relax period
Chart: Averaged light intensity vs. time (set 1)
Relax time period
Extend period
Fist period
One period
Transition period

## Slide 30: Fingerprinting the data
 | Delta ldr1 | Delta ldr2 | Delta ldr3 | Delta ldr4 | Delta ldr5
Extend |  | -25 | -80 | -200 | -10
Fist |  | -25 | -25 | -30 | 
One |  | 0 | -10 | -30 | 
I looked at several distinct sets of data for the same gesture series
Each sensor picks up different gestures differently
A simple average () is used to find the average for each gesture and relax period
Looking at the average between the several data sets, I found the sensor average of delta intensities as denoted at the right. The range of acceptable values for a sensor is determined as .
These distinguishable features can be used to determine the gesture in a given data set and be used for machine learning

## Slide 31: Possible questions
Why light as sensors? What else could you have used?
Cost?
Why only 3 gestures? How many more can you detect?
What else can this be used for?
Why is this important to have?

## Slide 33: Fiber optics
This is ideally less than the critical angle allowing light to be lost.
The refractive index of these materials cannot be measured without special equipment, but it can be used to understand the loss of light in the fiber
In my setup the cladding is simply Earth’s atmosphere

## Slide 34: LED Color xxx makes no sense
The optimal wavelength of the LDR must be determined
This does not depend on the material used
Humimic was used as a constant baseline due to its transparency
A 3d printed cast was used to eliminate external light
A constant depression was used to determine minimum intensity
Large red (630nm) and large blue (460nm) LEDs were determined to be the best. Red was chosen due to availability.
Colour | Medium | Minimum Intensity | Maximum Intensity | delta Intensity
Large blue | Humimic #2 | 160 | 990 | 830
Large red | Humimic #2 | 183 | 1013 | 830
Large white | Humimic #2 | 205 | 1021 | 816
Small red | Humimic #2 | 180 | 977 | 797
Large red | Earth's atmosphere | 235 | 996 | 761
Large yellow | Humimic #2 | 210 | 971 | 761
Small green | Humimic #2 | 189 | 937 | 748
Large blue | Earth's atmosphere | 228 | 957 | 729
Large green | Humimic #2 | 185 | 850 | 665
Small red | Earth's atmosphere | 245 | 864 | 619
Small green | Earth's atmosphere | 253 | 775 | 522
Large green | Earth's atmosphere | 240 | 720 | 480

## Slide 35: Key Questions
Pre Test
  What type of fiber material would work well?
    Must have imperfections that cause light loss due to deflection
    Must have consistent, reproduceable behavior
  What type of light should be transmitted?
    The LDR sensors work best with different light colors/wavelengths
  What shape of fibers work best?
Full prototype tests
  How are light levels impacted by different gestures?
  Can we uniquely identify different gestures using this approach?

## Slide 36: Materials/Mediums proposed
Standard optical fiber
Vytaflex – a semi-transparent urethane rubber
Ecoflex – an opaque silicone
Humimic gel – a transparent synthetic gelatin
Xxx why these 4?

## Slide 37: WHY WOULD IT WORK?
Transverse carpal ligament area
  Deflection occurs when fingers [tendons] are moved
  Magnitude of deflection of different tendons can be used to identify gestures
  6 different tendons in wrist
How to measure deflection accurately?
  Must measure all tendons and measure tiny (< 1 mm) movement
  Deploy a set of sensors across a watch strap
Notes: https://www.extremetech.com/mobile/285724-1-in-6-us-adults-now-own-a-smartwatch
https://arstechnica.com/gadgets/2019/09/apple-watch-series-5-hands-on-software-is-king/

## Slide 38: Problems with each material
Optic fibers were too perfect and there was no light deflection, even when bent over 90 degrees.
  The internal reflection is too high
  A non-ideal optical fiber is needed so that light is lost when bent
Ecoflex was too opaque and did not permit any light from the LED to pass
Humimic was too soft and melted/tore due to the body heat.
  Humimic melts at about 50 degrees; body heat is about 40
XXX what worked and how well…

## Slide 39: Different shapes tested
Tube
  Shrink tube: 20mm, 5mm, 4mm
  3d print: 2mm, 4mm, 5mm
  Straws: 3mm, 5mm
Sinusoidal  manufactured by first casting a mold using Vytaflex (Silicone)
Rectangular
Minimize the diameter to keep multiple strands for higher resolution
Sinusoidal and Rectangular molds required sensors to be embedded = fragility
Shrink tube and 3d printed molds caused capillary action (the material stuck to the sides)
Straws proved to be the best mold – 3mm proved to be best for LED shape and resolution

## Slide 40
Measure left to right and up and down on hand
35mm fibers vertically and 80mm horizontally

## Slide 41: Phase 3: Data analysis [Different Gestures xxx]
Chart: Light Intensity vs. Time
FINGER EXTENSION [EXTEND]

## Slide 42: PHASE 3: Handling Changing Readings
The baseline readings for a sensor can change over time
  E.g., due to movement of the wristband
Need to distinguish between changes due to gestures and changes in the baseline
Since changes due to gestures are short-lived, an exponentially-weighted moving average will ignore these changes
  determines how many “past values” to include in the average
    Small weighs past readings heavily
    Large makes the average closely track the current reading
Tuning to 0.05 and using a separate moving average of high and low values makes it possible to create a moving average that tracks the middle of the high and low values
Chart: Time (seconds)

## Slide 43: Labelling the data
Compare individual moving averages to original
Chart: Averaged light intensity vs. time
Time of determined maximum
Time of determined transition
Time of determined minimum

## Slide 44: Phase 3: data analysis [Extend] Labelling the data
Use moving averages
3 are used to find the maximum, minimum, and transition period
This is used to label the data (relax, transition, or extend)
The data is also labelled by hand
True negatives and true positives are determined
False points are labelled on the graph
Chart: 

## Slide 45: PHASE 1: proof of concept
Standard optical fiber
  Could not measure any light deflection
Ecoflex – an opaque silicone
  Too opaque and did not permit any light from the LED to pass
Humimic gel – a transparent synthetic gelatin
  Too soft. Melted even at body heat
Vytaflex – a semi-transparent urethane rubber
  Worked the best. Transmitted light the best and sturdy.
Mediums Tested
Fiber Shapes
Tube Molding Material | Pros | Cons
Shrink tube (20mm, 5mm, 4mm) | Somewhat easy to obtain, many sizes | Material stuck to sides Did not mold well
3D Printed Tube (2mm, 4mm, 5mm) | Customizable | Material stuck to sides Material could not be removed
Straw Mold Tube (3mm, 5mm) | Easy to obtain 3mm proved to be best for LED shape and resolution | 5mm proved to be too thick and inflexible
Rectangular | Easier to fabricate | sensors have to be embedded = fragile
Sinusoidal | Degree of light path independence between sensors | Sensors have to be embedded = fragile

## Slide 46: Pictures of materials and molds
Materials: Ecoflex, Humimic, Vytaflex, optical fiber
molds: Straws, heat shrink, 3d printed