## Slide 1: Lightweight assistive technology: A wearable, optical-fiber gesture recognition system
Sanjay Seshan Fox Chapel Area High School

## Slide 2: Objectives
18 years ago, a movie called Minority Report was first to introduce the world to a gesture-based interactive device.
Though common in science fiction and comic book movies, it is yet to become reality.
The goal of this project it to build a lightweight, low powered method to interact with computers around us
The computer will recognize a wide range of hand gestures
Does not require the use or special gloves or other intrusive hardware
Notes: Minority report

## Slide 3: CURRENT methods VS. Requirements
Current methods are
  Intrusive and cumbersome to wear (unnatural positions) – Tap, Cyber Glove, and other devices are uncomfortable and hard to put on and take off
  Impractical (e.g. camera based) – camera may not face the wearer, Google radar system is also off-body
  Prices range from $150 to $30,000
Must be wearable
Must be non-intrusive
Must be intuitive
Must be lightweight
Must be low-powered
Must be inexpensive
Tap
Cyber Glove
Notes: https://en.wikipedia.org/wiki/Wired_glove
https://www.youtube.com/watch?reload=9&v=mpbWQbkl8_g#t=810
https://towardsdatascience.com/training-a-neural-network-to-detect-gestures-with-opencv-in-python-e09b0a12bdf1
READ: https://www.wired.com/story/how-i-became-a-robot-in-london/

## Slide 4: Solution
Optical Fiber Based Lightweight Assistive Technology
Strap around the wrist
  1 in 6 adults own a smart watch
Use optical fibers as sensors along the strap to detect deflection
Transverse carpal ligament area
  Deflection occurs when fingers [tendons] are moved
  Magnitude of deflection of different tendons can be used to identify gestures
  6 different tendons in wrist  each corresponds to a finger
How to measure deflection accurately?
  Must measure all tendons and measure tiny (< 1 mm) movement
  Deploy a set of sensors across a watch strap

## Slide 5: Optical Fibers as Sensors
Optical fibers rely on the concept of total internal reflection to cause light to travel from one end of the fiber to the other
The refractive index of the material is determined by the ratio of the speed of light in the medium to a vacuum:
The angle at which total internal reflection occurs is:
For most glass fiber optics and , therefore
Notes: https://www.flickr.com/photos/brixendk/4349817216
Note that , which is almost the same as a vacuum (), so
https://www.flickr.com/photos/brixendk/4349817216
Note that 𝜈_𝑎𝑡𝑚𝑜𝑠𝑝ℎ𝑒𝑟𝑒=1.000350, which is almost the same as a vacuum (𝜈_𝑣𝑎𝑐𝑢𝑢𝑚=1), so 𝜃≈𝑎𝑟𝑐𝑠𝑖𝑛(1/𝜈_𝑚𝑒𝑑𝑖𝑢𝑚 )

## Slide 6: Optical Fibers as Sensors (continued)
If light strikes the fiber-atmosphere boundary at less than the critical angle it is completely reflected
Imperfections and rough surfaces within the fiber can cause light to be scattered and lost
This loss is made worse when the fiber is bent or deflected
If fibers were embedded in a wrist strap, deflection due to hand movement would cause characteristic changes in the amount of light transmitted
Analyzing the transmitted light levels could allow computers to reconstruct gestures!
“Lost” Light
“Transmitted” Light

## Slide 7: Basic setup for Deflection Sensor
Fiber/light medium
LED
Photoresistor / Light Dependent Resistor (LDR)
LED
Photoresistor/LDR
In order to detect the deflection using an LDR, a significant amount of light must be lost when the fiber is bent
35mm fiber length was determined to be the minimum for a noticeable light deflection when bent

## Slide 8: PROJECT METHODOLOGY
Step 1:
Proof of Concept
Step 2:
Prototype
Determine best material
Determine best shape
Determine color of LED light
Create a wearable band
Add sensors
Develop data collection method
Step 3:
Data Analysis
Measure how light levels are impacted by gestures
Uniquely identify different a selection of gestures
Automate process

## Slide 9: Step 1: Proof of CONCEPT
Designed a hard casing using Solidworks to test concept
3D Printed design for consistency and durability
Key features
  A holder for the medium to be placed in
  Lid to eliminate external light and isolated LED light
  Holder for LED and LDR on each end
  Plastic tool for consistent depression of medium
HARDWARE
Tool
Lid
Holder
LDR
LED
Medium
Lid
Tool
Holder

## Slide 10: Step 1: Proof of concept
The optimal wavelength for the Light Dependent Resistor (LDR) depends on the type of LDR used
For my Cadmium Sulfide LDR, Large red (630nm) and large blue (460nm) LEDs were determined to be the best (had the greatest delta intensity when depressed).
Red was chosen due to availability.
Meausrements in scaled light intensity (0-1023 which represents 0-5V)
Light Colors Tested
Colour | Medium/Fibre material | Minimum Intensity | Maximum Intensity | Delta Intensity
Large blue | Humimic #2 | 160 | 990 | 830
Large red | Humimic #2 | 183 | 1013 | 830
Large white | Humimic #2 | 205 | 1021 | 816
Small red | Humimic #2 | 180 | 977 | 797
Large red | Earth's atmosphere | 235 | 996 | 761
Large yellow | Humimic #2 | 210 | 971 | 761
Small green | Humimic #2 | 189 | 937 | 748
Large blue | Earth's atmosphere | 228 | 957 | 729
Large green | Humimic #2 | 185 | 850 | 665
Small red | Earth's atmosphere | 245 | 864 | 619
Small green | Earth's atmosphere | 253 | 775 | 522
Large green | Earth's atmosphere | 240 | 720 | 480

## Slide 11: Step 1: proof of concept
Smooth On Ecoflex (30) – an opaque silicone
  Too opaque and did not permit any light from the LED to pass
Humimic gel – a transparent synthetic gelatin
  Too soft. Melted even due to body heat
Smooth On Vytaflex (20) – a semi-transparent urethane rubber
  Worked the best. Transmitted light the best and sturdy. It also exhibited significant changes in intensity when depressed (~100).
Standard optical fiber (from Adafruit)
  Light intensity did not change with depression and was always at the maximum (1023)
Mediums Tested
Materials: Ecoflex, Humimic, Vytaflex, optical fiber

## Slide 12: Step 1: proof of concept
Fiber Shapes
Tube Molding Material | Pros | Cons
Shrink tube (20mm, 5mm, 4mm) | Somewhat easy to obtain, many sizes | Material stuck to sides Did not mold well
3D Printed Tube (2mm, 4mm, 5mm) | Customizable | Material stuck to sides Material could not be removed
Straw Mold Tube (3mm, 5mm) | Easy to obtain 3mm proved to be best for LED shape and resolution | 5mm proved to be too thick and inflexible
Rectangular | Easier to fabricate | sensors must be embedded  fragile
Sinusoidal | Degree of light path independence between sensors | Sensors must be embedded  fragile
Moulds: Straws, heat shrink, 3d printed, sinusoidal

## Slide 13: Step 2: prototype HARDWARE
Three 35mm and two 80mm Vytaflex fibers molded using 3mm straw
Large red (630nm) LEDs
LEDs and LDRs are fastened using heat shrink to the fiber
1 Arduino Uno
5 LDRs and 5 10k Ohm resistors
LED circuit: 9V battery, 5V regulator, 50 ohm resistor, 100 ohm resistor, Ohms resistors, 5 LEDs
35mm fibers
80mm fibers
LEDs
LDRs
1cm separation between fibers
1
5
2
3
4

## Slide 14: Step 2: ACTUAL HARDWARE SETUP
Setup on the previous slide is mounted with Velcro bands
The band is placed on the wrist
The Arduino is used to collect data
Code written in Python and C++
Arduino
Wrist strap

## Slide 15: Step 2: Gestures tested
A large collection of gestures can be tested using the prototype
I focus this presentation on three gestures
Finger Extension [Extend]
Finger Flexion
[Fist]
One Finger
[One]

## Slide 16: Step 3: DATA ANALYSIS
Light Intensity over Time
Manually Label Hand Position
Moving Averages vs. Original
Compute the Gesture Label
5 seconds of data was collected for each gesture
Includes a brief relax and transition period before and after gesture
Approximately 1 reading per 0.02s (250 readings/s)
Light intensity in scaled units (0 to 1023) based on the voltage drop due to the LDR (0 to 5V)
Compare

## Slide 17: Step 3: Data ANALYSIS [one finger]
Chart: Time (seconds)
Plot of scaled light intensity of each sensor over time as I repeatedly performed a one finger gesture
Each sensor (LDR) has its own unique baseline intensity value
  Each sensor need to be calibrated to a specific value separately
Each sensor detects the change in intensity when hand gestures are made
Chart: Time (seconds)
Relax position
One finger position

## Slide 18: Step 3: Handling Changing Readings
Graph of sensor 5 for the one finger gesture shows that the baseline readings for a sensor can change over time
  E.g., due to movement of the wristband
Need to distinguish between changes due to gestures and changes in the baseline
Two techniques to establish a baseline
Exponentially-weighted Moving Average: I use a moving average remove outliers and smooth noisy data
  determines how many “past values” to include in the average
    close to 0 weighs past readings heavily
    close to 1 makes average closely to current reading
    Tuning to 0.2 worked well
Sliding Window: I keep track of the maximum reading in the past 4 seconds. This (shown in red line) followed the changing reading well
Chart: Time

## Slide 19: Step 3: Identifying a Single Gesture
The graph shows readings of two sensors “normalized” by subtracting the average value of their readings (i.e. centering graph around value of 0)
Some sensors react more significantly to specific gestures
  Sensor 5 detects the deflection more intensely than sensor 1
By examining the magnitude of the change across all sensors, a unique “signature” can be determined for each type of gesture
Chart: Light Intensity for Repeated One Finger Gesture
Notes: Normalized Light Intensity

## Slide 20: Step 3: Creating a Gesture “Signature”
For each gesture, I manually labeled the data readings of a single trace as “Relax Baseline”, “Transition Between Relax and Gesture” and “Gesture” periods
I computed a simple average () reading of each period
I then computed the difference in Light Intensity between a Relax period and the subsequent Gesture period
This was done for each sensor and for each gesture
The table shows the average light intensity difference for each sensor/gesture
From this, I chose to use Sensors 2,3 and 4 to identify gestures
Chart: Time (seconds)
Relax
Gesture
Transition
Difference
 | Sensor 1 | Sensor 2 | Sensor 3 | Sensor 4 | Sensor 5
Extend | 8 | -48 | -90 | -223 | -12
Fist | 12 | -34 | -32 | -60 | 1
One | -3 | 2 | -24 | -49 | -4

## Slide 21: Step 3: Automatic Gesture Labeling
I collected sensor readings from two gestures of each type performed over 30 seconds
I used the computed signatures to automatically compute labels for each data point
  If the difference of the current reading from the baseline was within 10% of the signature value, it was assigned that label
  If the current reading was not within 10% of any label, it was marked as a “relax” (i.e. baseline gesture
  If the computed label had changed within the past 10 readings, the label was changed to “transition”
Chart: Time (seconds)
Chart: 
True Labels
Computed Labels

## Slide 22: Step 3: Labeling Accuracy
Accuracy of a classification system is typically summarized using a confusion matrix
The bulk of the computed classification are correct (highlighted along the diagonal)
The misclassification are mostly associated with the transition state
  Manual inspection suggested that these were associated slightly different estimates for the start/end of a gesture
  Note that there is some uncertainty in the true labeling of the transition state
  The impact of this misclassification on a gesture system is unlikely to be significant
 | Relax | Transition | Fist | Extend | One
Relax | 652 | 3 | 0 | 0 | 2
Transition | 62 | 83 | 14 | 17 | 21
Fist | 0 | 10 | 339 | 0 | 0
Extend | 0 | 8 | 0 | 206 | 0
One | 0 | 13 | 0 | 0 | 295
Computed Label
True Label

## Slide 23: Conclusions and next steps
Fiber optics are a practical method of detecting deflection in the wrist
This is inexpensive: LEDs, LDRs, resistors, and basic electronic equipment are ~$0.10 each, the Vytaflex is $27 for 0.91 kg (my setup uses roughly 4 mL or ~15 g), and the Arduino Uno is $19, so the total prototype cost was about $25-30.
The project is a promising first step in creating a light-weight assistive technology
The next step of the project is to increase the number of gestures recognized and complete the machine learning training on the data to auto-detect gestures
The final design for the wrist strap will be to have the system in a watch band and powered by a smart watch rather than an Arduino

## Slide 24: Appendix: code
int sensorPin = A0; // select the input pin for LDR(s)
int sensorPin2 = A1;
int sensorPin3 = A2;
int sensorPin4 = A3;
int sensorPin5 = A4;
int sensorValue = 0; // variable(s) to store the value coming from the sensor
int sensorValue2 = 0;
int sensorValue3 = 0;
int sensorValue4 = 0;
int sensorValue5 = 0;
void setup() {
Serial.begin(9600); //sets serial port for communication
pinMode(LED_BUILTIN, OUTPUT);
}
void loop() {
sensorValue = analogRead(sensorPin); // read the value(s) from the sensor(s)
sensorValue2 = analogRead(sensorPin2);
sensorValue3 = analogRead(sensorPin3);
sensorValue4 = analogRead(sensorPin4);
sensorValue5 = analogRead(sensorPin5);
Serial.print(sensorValue); //prints the values coming from the sensors on the screen
Serial.print(",");
Serial.print(sensorValue2);
Serial.print(",");
Serial.print(sensorValue3);
Serial.print(",");
Serial.print(sensorValue4);
Serial.print(",");
Serial.println(sensorValue5);
}
C++ Arduino Code

## Slide 25: code
#!/usr/bin/python
import serial
import time
import sys
# Determine the file to save data to and Arduino port
fileOut = sys.argv[2]
port = sys.argv[1]
f = open(fileOut, "w")
# Open Arduino serial
ser = serial.Serial(port, 9600, timeout=1)
def getData(timeout, label):
# measure delta time of a single gesture cycle for timeout
timeI = time.time()
while time.time()-timeI < timeout:
Python data collector

## Slide 26: code
try:
reading = ser.readline() # Read sensor values from Arduino
# Record delta Time, Unix time, ldr readings, and label to a file
data = [0,0,0,0,0,0,0,""]
data[0] = time.time()-timeIA
data[1] = time.time()
data[2] = int(reading.split('\n')[0].split(",")[0])
data[3] = int(reading.split('\n')[0].split(",")[1])
data[4] = int(reading.split('\n')[0].split(",")[2])
data[5] = int(reading.split('\n')[0].split(",")[3])
data[6] = int(reading.split('\n')[0].split(",")[4])
data[7] = label
for i in data:
print str(i)+",",
f.write(str(i)+",")
print ""
f.write("\n")
except:
pass
Python data collector cont.

## Slide 27: code
gestures = ["extend","fist","one"]*2 # declare labels of which gestrues are being tested
print("delta Time, Unix Time, pr1, pr2, pr3, pr4, pr5, label") # file headers
f.write("delta Time, Unix Time, pr1, pr2, pr3, pr4, pr5, label\n")
# Collect data for each gesture cycle for 5.0s
timeIA = time.time()
for gesture in gestures:
continueQ = raw_input("Do "+gesture+"? [Y/n]: ")
if continueQ == "y" or continueQ == "" or continueQ == "Y":
getData(5.0, gesture)
elif continueQ == "n" or continueQ == "N":
continueQ = "n"
f.close()
Python data collector cont.

## Slide 28: Appendix: Miscellaneous Pictures

## Slide 29: bIBLIOGRAPHY
To, Celeste, Tess Lee Hellebrekers, and Yong-Lae Park. "Highly Stretchable Optical Sensors for Pressure, Strain, and Curvature Measurement."
Meerbeek, I. M. Van, et al. “Soft Optoelectronic Sensory Foams with Proprioception.” Science Robotics, Science Robotics, 28 Nov. 2018, robotics.sciencemag.org/content/3/24/eaau2489.abstract.
Cho, Haedo, et al. "Design of an optical soft sensor for measuring fingertip force and contact recognition." International Journal of Control, Automation and Systems 15.1 (2017): 16-24.
Butt, Jawad Mehmood, Hesheng Wang, and Radan Pathan. "Design, Fabrication, and Analysis of a Sensorized Soft Robotic Gripper." 2018 IEEE 8th Annual International Conference on CYBER Technology in Automation, Control, and Intelligent Systems (CYBER). IEEE, 2018.
Chen, Wenbin, et al. "Fabrication and Dynamic Modeling of Bidirectional Bending Soft Actuator Integrated with Optical Waveguide Curvature Sensor." Soft robotics (2019).
Heintz, Brenner. “Training a Neural Network to Detect Gestures with OpenCV in Python.” Medium, Towards Data Science, 17 Dec. 2018, towardsdatascience.com/training-a-neural-network-to-detect-gestures-with-opencv-in-python-e09b0a12bdf1.
Poupyrev, Ivan. “Google I/O 2015.” Google, Google I/O Conference, 2015, www.youtube.com/watch?reload=9&v=mpbWQbkl8_g#t=810.

## Slide 30: Photo credit
https://orthoinfo.aaos.org/en/diseases--conditions/carpal-tunnel-syndrome/
https://www.semanticscholar.org/paper/Wrist-worn-hand-gesture-recognition-based-on-Zhu-Jiang/
https://thegadgetflow.com/
http://hyperphysics.phy-astr.gsu.edu/hbase/optmod/fibopt.html
http://oer2go.org/mods/en-boundless/www.boundless.com/physics/textbooks/boundless-physics-textbook/geometric-optics-24/reflection-refraction-and-dispersion-169/total-internal-reflection-and-fiber-optics-609-6258/index.html
https://en.wikipedia.org/wiki/Wired_glove
https://www.flickr.com/photos/brixendk/4349817216
https://www.amazon.com/
https://www.adafruit.com/
Minority Report (2002 Movie)
Sanjay Seshan